## Slide 1: Remote controlled fan boat
Design & documentation
by Timo Benzel
Tübingen, Germany

## Slide 2: Project goal
Design a remote controlled (RC) boat using electronic trash such as:
  an old hair dryer fan
  a servo motor to rotate the fan for steering
  two old 12V batteries
  two boards of styrofoam
  a 35MHz RC-sender and receiver from an old model airplane

## Slide 3: Requirements
the boat shall be built out of used parts or already available parts (it is basically a trash boat)
the boat has to always stay afloat for all maneuvers
the boat has to be steerable within a range of at least 50m
the boats thrust shall be controllable via remote control
the boat shall not disintegrate itself
the boat shall be made as fast as possible with the available parts

## Slide 4: Version 1 – Goal
Use a primitive setup for the proof-of-concept
  Use an emmiter circuit to control the power to the motor with PWM
  5V linear voltage regulator to power an Arduino Nano and the servo motor
  screw the fan directly on the servo‘s plastic mounting cross (you will find a way ;) )

## Slide 5: Version 1 – Parts used
old hair dryer fan
a servo motor to rotate the fan for steering
two old 12V batteries
two boards of styrofoam
a 35MHz RC-sender and receiver from an old model airplane
an Arduino nano
5V linear voltage regulator
Power MOSFET with 5V Vds threshold

## Slide 6: Version 1 – Build-up documentation
Start by cutting a hole in a small piece of wood/plywood on which the servo motor can be mounted
mount fan directly on servo using plastic screws from old eletronic devices
Mount the servo with the fan on top into hole

## Slide 7: Version 1 – Build-up documentation
Connect two old 12V batteries in series in order for the output voltage to be high enough to generate enough fan speed (if you have different batteries just try out how many you need in order to get the voltage high enough for the fan to get up to speed)
Get a small piece of perfboard and put the components on there according to the schematic

## Slide 8: Version 1 – Build-up documentation

## Slide 9: Version 1 – Build-up documentation
When you connect the plywood board to the styrofoam blocks always make sure you are using a clamping mechanism with tapping screws or use general purpose glue I clamped the two styrofoam pieces together with two sticks of wood through which i put wood screws
Careful: Test if your glue is corrosive to the styrofoam (e.g. superglue usually eat right thorugh styrofoam)
Version 1 taking a test swim in the bath tub

## Slide 10: Version 1 – Validation
The boat stays afloat  requirement fullfilled
Boat is steerable and thrust controllable
The boat is built out of old/used parts

## Slide 11: Version 1 – Validation
the boats crossection was quite large and non-hydrodynamically shaped, so the bow wave was especially prominent
which caused
  increased drag
  water spilling into the cavity of the styrofoam blocks underneath the electronics (not too bad, but not ok)
  smaller max. velocity (ironically especially when thrust is high)

## Slide 12: Version 1 – Validation
The 5V linear voltage regulator reached >60°C even with a huge heat sink, especially when the servo was used a lot This temperature was considered to be too high
In version 1 the antenna was wound up into a ring which decreased the range of good reception to only about 10m; beyond this range the controls would start acting up

## Slide 13: Version 2 – Goals
This version needs to have the ability to generate reverse thrust
Improvements on the previous design:
  less drag due to smaller crosssection due to the katamaran design
  instead of the use a full-bridge inverter design to create the possiblity of inverting the motor voltages and thus the capability to reverse thrust
  replace the linear voltage regulator with a DC-DC step-down converter to generate the 5V with fewer losses and thus smaller temperatures

## Slide 14: Version 2 – Build-up documentation
The overall wiring of version 2

## Slide 15: Version 2 – Build-up documentation
The plywood board was screwed onto two wooden bars, one on each side
The wooden bars would be pushed against the styrofoam with screws supported by washers and cardboard on the ofter side of the foam block
The antenna would be would around a thick wire fixed to the styrofoam to maximize ist straight length to increase reception

## Slide 16: Version 2 – Build-up documentation
Usually these hair dryer fans work with AC voltage, which is why they have a rectifier attached between the power supply and the connectors to the brushes  now that we want to apply negative voltages to the motor, we need to remove the rectifier But: leave the intermediate circuit capcitor on there. It makes sure, that the high voltage sparks from the brushes does not affect your power electronics too much

## Slide 17: Version 2 – Validation
The range is much larger now > 20m  the straighened antenna design works well
the fan was facing upward which caused a torque pushing down the bow of the boat which still caused:
  increased drag
  smaller max. velocity (ironically especially
  less thrust being directed forward but downward
fan
thrust
Forward thrust
Upward thrust
Torque due to upward thrust

## Slide 18: Version 2 – Validation
The RC receiver got damaged after the validation at home (reason unknown)
  Symptom: All control signals behaved erratic
  Root cause lies in the receiver
  Origin might be the voltage harmonics in the DC-DC converter, that might have damaged the receiver  35 MHz RC system needs to be replaced with 2,4 Ghz system (more robust when it comes to disturbances)

## Slide 19: Version 2 – Validation
Power supply output filter needs to be installed because the 5V voltage output of the DC-DC converter ripples dramatically with a 2Vpp value at 80 kHz this behavior might damage other components as well

## Slide 20: Version 3 – Goals
this version needs to have the fan tilted downwards, such that the bow is rising out of the water
power supply output filter needs to be installed because the voltage ripples of 2Vpp are too large
replace the 35Mhz RC system with 2,4 GHz system

## Slide 21: Version 3 – Build-up
Power supply output filter needs to be installed
  R-C-lowpass filter with a 330µF capacitor and a 7 Ohm resistor we get Hz which is enough telling from the voltage plot over time
No lowpass
69Hz-lowpass

## Slide 22: Version 3 – Build-up